Installation of SMR 40200-Kit

- Remove the following parts (hence unneeded):

- DZ 801 zener diode at secondary  size ( if short circuit )

- SMR 40200 IC, HIS 0169B  ( or C ) hybrid, R 801 ( 0,33 (/ 5W )

- C 803 ( 2,2nF/ 800V )

- Solder SMPS trafo “7” pin ( =SMR40200 IC “1” pin ) to primary ground (for example                               C801 elko – pin ).  Attention: At the original schematic SMPS trafo “6”-“7” pins have been changed!

- Mount  the Kit to the original place of  SMR40200 IC (don’t forget to screw the Fet to the heat sink)

- Solder the RED wire of Kit to +300V ( for example C801 elko + pin )

- Solder the BLACK wire of Kit to ~230V ( for example D801 Greatz-bridge ~ input )

- Adjust system voltage to A2= 125V ( with SMR Kit potmeter )                                           / Stand-by A2= approx. 145V /

Note: For working of SMR Kit need only +300V from the chassis, so any (defected) part from primary side does not affect the working.